Procedure for Using the Temperature Controller of the Blue Furnace

- To start from off mode, press return, last and yes.

- Press param check to skip Manuel Control 1, Manuel Control 2, Arrow Keys Off and Tune Outputs.

- Arrive at Profile A and press yes.

- Press param check to skip Delay A. You can use the up and down arrows to adjust the time that you want the program to delay.

- Arrive at SP A00. This is the starting temperature. We usually leave it at room temperature. You can leave in at any number because it doesn’t matter. Remember the unit is Fahrenheit.

- Press param check and arrive at Time A01.

  - Use the up and down arrows to adjust the time that you want the furnace to take to raise the temperature from SP A00 to SP A01 (which you will set in the next step). Remember the unit is Minute: Second.

  - If you don’t care about the ramping rate, leave it at Cont as continue.

- Press param check and arrive at SP A01. Use the up and down arrows to adjust the temperature that you want.

- Press param check to arrive at Time A02.

  - Leave it at 0:00 if you don’t need another temperature.

  - Adjust it at Cont. if you want the temperature to rise to another point.

  - Adjust it to the time that you want if you want to rise the temperature again in a controlled manner.

  - In both cases of b and c, continue on by pressing param check to do the same thing as you set up the first segment of the program, until you reach the Time A0# that you don’t need anymore.

- Press display to arrive at the display screen.

- Press start to run the program.

Note: Do not program Profile B, which is set for the cathode annealing.

The buttons are in blue and the screen displays are in red.

Please let Lei An know if you have any questions about the furnace.

Thank you for your cooperation.